## Slide 1
Reah flisakowski
transportation engineer
rlf@dksassociates.com
503.243.3500
Introduction to transportation engineering and community planning
Oregon city
planning commission
work session

## Slide 2
agenda
/ team Introduction
/ long-term transportation planning
/ transportation analysis for development review

## Slide 3
Team introduction

## Slide 4
DKS support staff
Reah Flisakowski, PE
Senior transportation engineer
B.S. civil engineering
23 Years Experience at DKS
on-call development review services multiple agencies and long-range community planning
Oregon city planning commission work session
4
Kevin chewuk, PTP
Senior transportation planner
B.S. transportation planning, M.S Urban & regional planning
14 Years Experience at DKS
on-call development review services multiple agencies
Oregon City TSP, SDC update, several local plans
Amanda deering, PE
transportation engineer
B.S/M.S. civil engineering
6 Years Experience at DKS
on-call development review services multiple agencies
Thimble creek concept plan, I-205 tolling review

## Slide 5
long-term transportation planning

## Slide 6
Identify policies and projects in Oregon City:
Oregon Highway Plan, Oregon Transportation Commission
Oregon Transportation Planning Rule
Metro Regional Transportation Plan
Clackamas County Transportation System Plan
Oregon City Transportation System Plan
Transportation plans
Oregon city planning commission work session
6

## Slide 7
Oregon city planning commission work session
7
planning context
Oregon City TSP Goals
  Enhance health and safety for residents
  Emphasize effective and efficient management of the system
  Foster a sustainable system
  Provide an equitable, balanced and connected multimodal system
  Identify solutions and funding to meet needs
  Increase the convenience and availability of pedestrian, bicycle and transit modes
  Ensure the system supports a prosperous and competitive economy
  Comply with state and regional plans
Comprehensive Plan vision for 2040
Healthy and welcoming community
Diverse economy
Connected infrastructure
Protected environment

## Slide 8
Oregon city planning commission work session
8
TSP addresses long-range system needs across the city
Development review addresses short-term impacts in local area
estimated growth
Source: City of Oregon city tsp – based on population and metro land use forecasts

## Slide 9
Regulations
  Goals and Policies
  Design Standards
  Development Code
Projects ($200M+)
  Master Plans for all modes of travel with priorities
Outcomes of the tsp
Oregon city planning commission work session
13
Funding ($73M)
  Gas Tax Revenues
  System Development Charges
  Development Contributions
  New Vehicle Registration Fee
  80%

## Slide 10
Transportation analysis for development review

## Slide 11
Transportation analyses are required to provide an objective assessment of potential impacts from a specific land use action (development application, zone change or comp plan amendment).
Key Questions to Answer with TIS:
Will the existing system accommodate the proposed development from a vehicle operation and safety standpoint?
How will study intersections operate relative to the City’s mobility standards?
What on-site and off-site improvements will be necessary to support the development? Are they TSP projects?
How will access to the development affect nearby traffic operations?
How will the development ensure safe and efficient circulation on and adjacent to the project site?
How will the development provide needed walking, biking, transit and driving connections to adjacent parcels?
Transportation impact study (TIS)
Oregon city planning commission work session
11

## Slide 12
General Steps to Conduct a TIS:
Determine scope of analysis
  study locations (arterial and/or collector intersection, add 20+ trips/hour)
  Year of opening (or phases) and time of day
Evaluate system performance
  Data collection – intersection counts, system inventory
  Estimate new trips, evaluate intersection operations, need for new connections, safety issues, evaluate site access
  Compare conditions without and with development to measure impact
Recommend mitigations to address impact if standards are not met
  Construct off-site improvement (intersection capacity)
  Construct improvements along the site frontage
  Pay fees toward planned system improvements (SDC, proportionate share)
TIS Guidelines and procedures
Oregon city planning commission work session
12

## Slide 13
trip generation
Oregon city planning commission work session
13
Estimate New Trips
  ITE trip rates based on national surveys
  Land use categories for all types of development (recent update)
  Development size (building square-foot, housing units)
  Rates for peak hour and daily trips
  Allowable trip reductions – mixed use, low income

## Slide 14
Intersection volumes
Oregon city planning commission work session
14
Estimate Where New Trips will Travel
  Local knowledge and travel forecast model
  Percentage assigned to nearby system
  New trips added to study intersections
Estimate Background Growth
  In-process trips approved by City but not constructed
  Trips from growth outside City

## Slide 15
Mobility standards
Oregon city planning commission work session
15
Evaluating Intersection Operations – Is there an impact?
Level of service (LOS) measures intersection vehicle delay (LOS A to F)
Volume-to-capacity ratio (v/c) measures how much capacity is used (0 to 1.0)
Different standards for control type (signal, unsignalized) and location (Metro RTP arterial and OC Regional Center)
During evening peak hour: LOS D at OR 213/Molalla Ave/Douglas Loop and LOS F at OR 213/Beavercreek Rd

## Slide 16
Safety assessment
Oregon city planning commission work session
16
    Evaluate historical collision data (last 4 years) at study intersections
    Identify collision trends and potential safety issues with adding new trips

## Slide 17
Access evaluation
Oregon city planning commission work session
17
    Access Spacing Standards
    Based on functional classification and fronting land use (residential, commercial, industrial)
    Maximum and minimum block length and intersection spacing, minimum driveway spacing, minimum traffic signal spacing
    Sight Distance Standards
    Based on travel speeds and on-site measurements

## Slide 18
Conditions of approval
Oregon city planning commission work session
18
If new trips are expected to impact vehicle operations or safety and standards are not met, the development is responsible to mitigate the impact
Common mitigations:
Offsite intersection capacity improvement (turn lane, signal)
Provide street stub to adjacent property
Relocate access location or restrict access (right in/right out)
Needs to be proportional to the impact
Is the capacity or safety need existing?
Consider the number of new trips v. level of mitigation

## Slide 19
Allowed when criteria below are met:
Fewer than 24 peak hour trips and 250 daily trips (examples: 24 single-family homes, 15,000 SF office)
AND
Not expected to further impact an intersection operating below City mobility standard or with safety concerns
  Minimal requirements:
  Trip generation estimate
  Evaluate proposed accesses – spacing standard, sight distance, circulation and safety
Transportation analysis letter (TAL)
Oregon city planning commission work session
19

## Slide 20
Thank you

## Slide 21
Oregon city standards
Oregon city planning commission work session
21
Mobility Standard - Peak Hour
  Signalized
    Intersection LOS D or better
    Each approach LOS E and volume to capacity ratio <1.0
  Unsignalized
    All movements LOS E or better
    Low volume movements (<20 veh) LOS F
    RTP Arterial Network: v/c < 1.0
    OC Regional Center: v/c < 1.1
    OR 213/Beavercreek Rd: v/c <1.0

## Slide 22
Examples: rezones, master plans
Triggers OAR 0060 Transportation Planning Rule (TPR) assessment
Evaluate impact in the long-term planning horizon to see if TSP modifications are necessary to accommodate the proposal
  What is the growth increment from the proposed use (reasonable worst-case for land designation changes) compared to the planned use?
  How will the system perform with the proposed change compared to the adopted plan?
  Are additional system improvements (including all modes) necessary to accommodate the proposal?
Zone Changes/
Transportation Plan Modifications
Oregon city planning commission work session
22

## Slide 23
Project Life Cycle
    Master Plan Project List
    CIP programming or development mitigation
    Project development (design and bidding)
    Construction
    Maintenance / Operations
How are infrastructure projects implemented?
Oregon city planning commission work session
23

## Slide 24
System Development Charges
  Spreading the cost of development-driven infrastructure across all future development
  Helps fund known long-range projects
Development Mitigation / Exactions
  Requiring a specific development to fully fund (or contribute to) an improvement
  Addresses near-term project needs
How are projects funded?
24
Existing User Contributions
  Gas taxes, general fund, etc.
Other Potential Sources
  Urban Renewal, LIDs, Utility Fees, G.O. Bonds, and Grants
Oregon city planning commission work session